## Slide 1: Lessons Learned Dust Emphasis Team Inspections On-Shift Examinations
By Roy Baker
District 4 Health Supervisor

## Slide 2: Part 75 – 75.362 (a)(2) On-shift Examinations
Examination to assure compliance with respirable dust controls in the Approved Ventilation Plan
  Within 1 hour of shift change if there is no break in production (Hot-Seating)
  Prior to resuming production if there is a break in production at shift change
Deficiencies corrected prior to production beginning or resuming

## Slide 3: Part 75 – 75.362 (a)(2) On-shift Examinations
Examination includes:
  Air quantities and velocities
  Water pressures & flow rate
  Excessive leakage in water delivery system
  Water spray number and orientation
  Section ventilation & control device placement
  Work practices in plan
  Any other dust suppression measures

## Slide 4: Part 75 – 75.362 (g)(2) On-shift Examinations
  Certified person conducting the on-shift examination to assure compliance with the respirable dust control parameters was not certifying by initials, date, and time that the examination was made.

## Slide 5: Water Spray System Examination
  Sprays used were not approved in the plan
  Water flow rate incorrect
  Pressure was not being checked on both sides of the Continuous Miner and multiple locations on Longwall
  Dirty sprays were producing an ineffective spray pattern

## Slide 6: Scrubber Examination
Full Pitot Traverse checks of the scrubber were not being conducted and some folks did not know how to conduct the required checks or how to establish a centerline correlation factor (Average velocity divided by centerline reading) for use throughout the week for a comparison depending on your plan requirements.
Scrubber sprays were not being checked to make sure they were working and covering the entire area of the screen.
Different size screens were being used besides what the plan required. Examples- 20 mesh,30 mesh, or bottle brush type
Seals around screen doors and demister were missing or damaged.
The bottom of sumps were found clogged.
Deflector vents were damaged to keep from directing exhaust toward ribs and a few were found missing.

## Slide 7: On-shift Parameter check of Roof Bolting Machines

## Slide 8
MSHA Approved Dust Hose

## Slide 9
Check for and Fix Any Leaks
Check for Hose Wear and Replace if Required
Hose Clamps – Installed and Tight
INSPECTION AND MAINTENANCE - DUST HOSE, FITTINGS AND CLAMPS

## Slide 10
INSPECTION AND MAINTENANCE
DUST BOXES AND FILTER ELEMENTS...
Door Latches
If damaged replace with Fletcher OEM dust tank latch only.

## Slide 11
Doors
and Door Gaskets
Doors not warped or bent
All gaskets installed, in good condition and clean.
Each chamber must be separated. Check for air leaks and replace gasket if necessary.
Use only OEM gaskets

## Slide 12
Filter Elements
Make sure filter sealing surface is clean
If dust bypasses filter, this cavity must be cleaned out or system will not operate properly.
Never attempt to clean filter elements.
Remove and properly dispose of dirty element.
Install new approved element when dust collection efficiency decreases to the point that drilling rate is reduced. Clean box area of dust before installing new clean filter or dust can contaminate clean side of system.
Hand tighten wing nut as tight as possible
Dust leakage around nut is possible if not tight

## Slide 13
MAKE SURE HOSES ARE CONNECTED CORRECTLY
AIRFLOW DIRECTION ARROWS
PN: 56362
Cyclone Cap

## Slide 14
Roy Baker
District 4
Mt. Hope WV.
PH# 304-877-3900
baker.roy@dol.gov

## Slide 15
DAVID STEFFEY
CLR – DISTRICT 5
NORTON, VA
LESSONS LEARNED
DUST EMPHASIS TEAM INSPECTION FINDINGS
WATER DELIVERY SYSTEMS

## Slide 16: FINDINGS OF THE DUST EMPHASIS TEAMS
Water delivery system problems found
  Inadequate water pressure
    Undersized pump
    High resistance in pipe system
  Inadequate water volume
    Too small diameter water line
  Poor water delivery to face equipment
    Hose size
    Piping on machine
    Wrong sprays

## Slide 17: FINDINGS OF THE DUST EMPHASIS TEAMS (cont.)
  Water related Dust Controls Specified in Ventilation Plan are Ambiguous
  Type of water sprays cover wide range of options – can not be evaluated
    Specify BD-2, BD-3, BD-5 can be used
    Spray flow rates 0.42 gpm to 1.6 gpm
    Spray type 3
    Spray XX or equivalent

## Slide 18: FINDINGS OF THE DUST EMPHASIS TEAMS (cont.)
  Water sprays
    Required sprays not used
    Lower water flow rate
    Lower water pressure
    Sprays are not maintained – dirty, do not produce spray pattern

## Slide 19
Quickly Recognizing Problems Can Maintain Nozzle Performance, Quality and Efficiency
Seven Reasons Why Nozzles Don’t Perform Properly
  Erosion and nozzle wear
    Wear of the nozzle orifice and internal flow passages
    As a result flow is usually increased, pressure may be decreased and the pattern may become irregular
    Nozzles should be checked with a pressure gage and flow meter – when flow rate is 15% above published value this nozzle should be changed
  Corrosion
    Nozzle surface breaks down due to chemical action of sprayed material or environment
    Nozzles that are corroded should be changed
    Certain materials used to produce nozzles are more durable than others
    Choose your nozzle based on in mine conditions
  High temperature – Not usually a factor in coal mining

## Slide 20
  Caking or bearding
    Build up of material on the orifice due to liquid evaporation
    Water quality can greatly affect this (hard water)
    Typically a problem with atomizing nozzles
    Caked nozzles should be replaced
  Damage
    Damage to the orifice can occur when improper cleaning tools are used
    Meaning – nails are not good for cleaning nozzles
  Clogging
    Material clogs the orifice and the spray pattern is not evenly distributed
    Good filtration systems can help avoid this
  Improper Assembly
    Some nozzles require careful reassembly after cleaning
    Simplicity of maintenance should be considered (the fewer the parts the better)

## Slide 21
SOURCE OF THE MINE WATER
  Public
  Water storage tank
  Surface water – pond/stream
FILTRATION TO MAINTAIN A CLEAN WATER SUPPLY
  At source
  On MMU
  Maintain filtration system
Considerations when Ensuring Water Delivery System Meets Plan Requirements

## Slide 22
  Other Considerations
    Number and Type of MMU’s you will use
      Continuous Miner
        Dust suppression sprays
        Scrubber
        Wethead Miner
      Longwall
    Other Water Needs
      Belt transfer points
      Regulatory requirements for fire fighting

## Slide 23
DAVID STEFFEY
CLR – DISTRICT 5
NORTON, VA
Steffey.David@dol.gov

## Slide 24: Lessons Learned Dust Inspections
By Brent Wolfe
Health Specialist
District 3

## Slide 25: Operator Sampling Program
Sampling Unit
  Equipment (sampling units) not maintained as approved
  Flow rates not maintained at 2.0 L.P.M.
  Sampling head assemblies are not cleaned and inspected
  Pre-sampling shift checks :
    Black hose used
    No voltage checks made
    Pump and apparatus assembled prior to 3 hours before the start of the start of shift
Sampling Procedures
  Respirable dust samples are not collected at required times (shifts/days)
    Example : 14 days to take 5 valid samples with full production, 3 shifts a day.

## Slide 26: Operator Sampling Program
Sampling Procedures
  Certified persons do not know the regulatory requirements for the proper collection of respirable dust samples
    A Control Filter sent in as a Regular Sample
    1 Control Sample sent in for 5 separate respirable dust samples
  Improper record keeping for length of shift
  Maintaining sample in appropriate location:
  Belt DA Sample found too far away
  Operating sampling unit portal-to-portal
  Full Shift Sampling

## Slide 27: Air Quantity
Air at end of curtain does not match plan
  Example: Lower air quantity due to curtain found 16” off the mine floor.
Air not balanced with scrubber quantity (blowing face)
  Example: To much air quantity at end of line curtain (More than limits of Plan).

## Slide 28: Dust Scrubber
Scrubber quantity lower than plan quantity
Air quantity measurements performed incorrectly
  Plugs in Pitot holes
  Not testing all Pitot holes
  Holes between scrubber screen sprays and screen

## Slide 29: Dust Scrubber
Ductwork dirty/plugged
Screens not dried per Plan
Demisters found with 1 inch thick sediment on layer filaments
Sump pump not working

## Slide 30: Roof Bolter Dust Collectors
Dust box door seals not maintained - Non-approved seals
  Ex. weather stripping from home improvement store
Vacuum hoses do not match approval requirements and found leaking
“Clean“ side of collector contaminated
Dust box door latches not maintained
Vacuum setting does not meet approval plate

## Slide 31: Roof Bolter Dust Collectors
  Non-Approved Hoses being used ( electrical conduit)
  Electrical tape covering up holes
  Clean Side of system contaminated with white fine dust
  Latches missing; Door hinges broke; Mine sealant used to seal door.
  Vacuum pressures to low, Hoses not clamped onto barbed connector’s.

## Slide 32: Roof Bolter Dust Collectors
Valves installed in the dust collection system.
Low pressure found when valve to dust collection box turned off.
Door Seals “pieced” together with and without approved seals.

## Slide 33: Dust Controls not being Maintained According to Approved Ventilation Plan
Water sprays
  Required sprays not used (1MM sprays used instead of 3/32”)
  Lower water pressure (dirty filters, inside of hoses collapsed).
  Sprays not maintained—dirty, do not produce spray pattern.

## Slide 34: Dust Controls not being Maintained According to Approved Ventilation Plan
Mag Gauges not maintained
Holes on adapters of Mag Gauges plugged with dirt/sediment
Loose adapters on Mag Gauges
CMO’s do not know Plan requirements (Scrubber screen needs cleaned every 40 feet of advancement).